## Slide 1: Dr.SNS RAJALAKSHMI COLLEGE OF ARTS AND SCIENCE (AUTONOMOUS) COIMBATORE-641049 Accredited by NAAC(Cycle III) with “A+” Grade Recognised by UGC, Approved by AICTE, New Delhi and Affiliated to Bharathiar University, Coimbatore.
DEPARTMENT OF COMPUTER SCIENCE
21PCS101:Artificial Intelligence for Robotics
I YEAR - I SEM
TOPIC – Subsumption Architecture
UNIT 2 – Subsumption Architecture

## Slide 2: Subsumption Architecture
Subsumption architecture was originally described by Dr. Rodney Brooks, a professor at MIT, who would later help found iRobot Corporation and invent the Baxter Robot.
Rodney was trying to develop analogues of insect brains in order to understand how to program intelligent robots.
The basic concept of subsumption has been around for some time, and it has been adapted, reused, refined, and simplified

## Slide 3: Subsumption Architecture
The first aspect to understand is that we want our robot to act on a series of goals. The robot is not simply reacting to each stimulus in total isolation, but is rather carrying out some sort of goal-oriented behavior.
The goal may be to pick up a toy, or navigate the room, avoiding obstacles. The paradigm we are creating has the user set goals for the robot and the robot determine how to carry those goals out, even if the goal is simply to move one meterforward.

## Slide 4: Subsumption Architecture
The first aspect to understand is that we want our robot to act on a series of goals. The robot is not simply reacting to each stimulus in total isolation, but is rather carrying out some sort of goal-oriented behavior.
The goal may be to pick up a toy, or navigate the room, avoiding obstacles. The paradigm we are creating has the user set goals for the robot and the robot determine how to carry those goals out, even if the goal is simply to move one meterforward.

## Slide 5: Subsumption Architecture
The problem begins when the robot has to keep more than one goal in mind at a time.
How do we arbitrate between different goals, to determine which one has precedence?
The answer is found in the following diagram:

## Slide 6: Subsumption Architecture
The robot's decision-making systems into three layers.
Each layer has a different level of responsibility and operates on a different time scale.
At the lowest levels are what we might call the robot's autonomic nervous system – it contains the robot's internal health-keeping and monitoring functions.
These processes run very fast – 20 times a second or so, and only deal with what is inside the robot.
This would include reading internal sensors, checking battery levels, and reading and responding to heartbeat messages.
I've labeled this level take care of myself.

## Slide 7: Subsumption Architecture
The next level handles individual tasks, such as driving around, or looking for toys.
These tasks are short term and deal with what the sensors can see.
The time period for decisions is in the second range, so these tasks might have one or two hertz update rates, but slower than the internal checks.
I call this level complete the task – you might call it drive the vehicle or operate the payload.

## Slide 8: Subsumption Architecture
The final and top level is the section devoted to completing the mission, and it deals with the overall purpose of the robot.
This level has the overall state machine for finding toys, picking them up, and then putting them away, which is the mission of this robot.
This level also deals with interacting with humans and responding to commands.
The top level works on tasks that take minutes, or even hours, to complete.

## Slide 9: Subsumption Architecture
The rules of the subsumption architecture – and even where it gets its name – have to do with the priority and interaction of the processes in these layers.
The rules are as follows
Each layer can only talk to the layers next to it.
The top layer talks only to the middle layer, and the bottom layer also talks only to the middle layer.
The middle layer can communicate with either.

## Slide 10: Subsumption Architecture
The rules of the subsumption architecture – and even where it gets its name – have to do with the priority and interaction of the processes in these layers.
The rules are as follows
The layer with the lower level has the highest priority.
The lower level has the ability to interrupt or override the commands from higher layers.

## Slide 11: Subsumption Architecture
The major benefit of this type of organization is that it keeps procedures clear as to which events, faults, or commands take precedence over others, and prevents the robot from getting stuck in an indecision loop.
Each type of robot may have different numbers of layers in their architecture. You could even have a supervisory layer that controls a number of other robots and has goals for the robots as a team.
The most I have had so far has been five, for one of my self-driving car projects.