## Slide 1: Dr.SNS RAJALAKSHMI COLLEGE OF ARTS AND SCIENCE (AUTONOMOUS) COIMBATORE-641049 Accredited by NAAC(Cycle III) with “A+” Grade Recognised by UGC, Approved by AICTE, New Delhi and Affiliated to Bharathiar University, Coimbatore.
DEPARTMENT OF COMPUTER SCIENCE
21PCS101:Artificial Intelligence for Robotics
I YEAR - I SEM
TOPIC – Picking up the Toys
UNIT 4 – Picking up the Toys

## Slide 2: Outline
Task analysis
Teaching the robot arm
Other robot arm machine-learning approaches

## Slide 3: Technical Requirements
It will be using Python with NumPy, the matplotlib library to make plots and graphs, and the pickle library to store data.

## Slide 4: Task Analysis
We have a mobile base with a six degree-of-freedom arm attached to it. We are fortunate that TinMan's robot arm is constructed out of servo motors. We can tell where all of the parts of the arm are if we know where the servos are commanded to be, since we are commanding the angles of the servos. We can use forward kinematics, which is to sum up all the angles and levers of the arm in order to deduce where the hand is located at.

## Slide 5: Task Analysis

## Slide 6: Task Analysis
We want the robot to figure out what it takes to get to that position. We need to give the robot a way to test out different theories, or actions that will result in the arm moving.
We will also do the hand rotating, and the fingers opening and closing later as part of a different process when we learn how to grasp objects.

## Slide 7: Task Analysis
That leaves us with an action space with just three actions – setting the position of the three middle servomotors, which I will call shoulder pitch, elbow pitch, and wrist pitch.
Our possible actions are shoulder pitch from 0 to 180, elbow pitch from 0 to 180, and wrist pitch from 0 to 180. This produces a large range of motion from just these three motors.

## Slide 8: Setting up the solution
We will call the act of setting the motors to a different position an action, and we will call the resulting position of the robot hand the state.
We are going to have the robot associate states (a beginning position of the hand) and an action (the motor commands used when at that state) with the probability of generating either a positive or negative outcome – we will be training the robot to figure out which sets of actions result in maximizing the reward.

## Slide 9: Setting up the solution
We will use some of the same tools we used before in our neural network to propagate a reward to each step in a chain of movements that result in the hand moving to some location. In reinforcement learning circles, this is called discounting the reward – distributing portions of rewards to the step in a multi-step process.
Likewise, the combination of a state and an action is called a policy – because we are telling the robot, when you are in this position, and want to go to that position, do this action.

## Slide 10: Setting up the solution

## Slide 11: Setting up the solution
Our process for learning with the robot arm will look like this – we will set a goal position for the robot arm. We can start by saying we have four arm positions we want – neutral carry, pick up, high carry, and drop off.
These are our starting four positions. We can add more later if it looks like we need them:

## Slide 12: Setting up the solution

## Slide 13: Setting up the solution
We calculate rewards using the Q-function. Q represents the reward the robot will be getting (or expecting to get) from a particular action.
Where Q(s,a) is the final reward for an action given the starting state, reward(s,a) is the reward for that action, g is a discount function that rewards getting to the goal quicker, and max(Q(s’,a’) selects the action that results in the largest reward out of the set of actions available at that state. In the equation, s and a represent the current state and action, and s’ and a’ represent the next state and next action.

## Slide 14: How do we pick actions?
What actions can the robot arm perform? We have three motors, and we have three options for each motor. We can do nothing – that is, not move at all. We can move counterclockwise, which will make our motor angle smaller, and we can move clockwise, which makes our motor angle larger.
Note: most servo motors treat positive position changes as clockwise rotation. Thus, if we command the rotation to change from 200 to 250 degrees, the motor will turn clockwise 50 degrees.

## Slide 15: How do we pick actions?
Our action space for each motion of the robot arm is to move each motor either left, right, or not at all. This gives us 27 combinations with three motors (3 x 3 x 3 possible actions). We will note this with an action matrix.
Each action will have three values. An action that reduces the angle of motor 1, holds motor 2 in place, and increases motor 3, noted by [-1, 0,1]. We will just use 1 in the action matrix because we will set the magnitude of the motion in another way. The x-y coordinates of the hand can be computed from the sums of the joints.

## Slide 16: How do we pick actions?
Another way of looking at this process is that we are generating a decision tree.
When we move motor 1, motors 2 and 3 move position in space, and their angles and distances to the ground and to our goal change.
Each possible motor move adds 27 new branches to our decision tree, and can generate 27 new arm positions. All we have to do is pick which one to keep.

## Slide 17: Summary of robot arm learning
We have reinforcement learning in the process of maximizing rewards. We are using Q-learning to compute rewards for successful completion or partial completion of a goal.
We use a straight artificial neural network (ANN) to predict the outcomes of actions given a beginning state.
And we introduced genetic algorithms to innovate and make movement patterns that we can teach to the robot arm:

## Slide 18: Summary of robot arm learning

## Slide 19: Summary of robot arm learning
Our general process for teaching the arm how to move is based on a type of reinforcement learning called Q-Learning. Our concepts are summarized in the following equation:
Q(s,a) = R(s,a) + G max[Qst+1,a]
Here, Q(s,a) is the value of an action done in a particular state.
R is the reward given for that action.

## Slide 20: Summary of robot arm learning
G is a discount factor that reduces rewards for longer sets of actions.
G is normally set to a number less than 1, like .9. For example, a set of actions that reaches the goal in 10 steps (actions) gets a higher Q than a set of actions that takes 20 steps. The function max[Qst+1,a] says to look at the next state of the robot, and select the action that results in the highest Q value for the next state.

## Slide 21: Teaching the robot arm
Servo motors are commanded by setting an angle for the motor’s output shaft to assume. The angles run from 0 to 180 degrees. However, the commands for the motor positions run from 1 to 255, so they fit into a single 8-bit value. We’ll be converting these byte-based motor commands to and from angles in the program.

## Slide 22: Teaching the robot arm
Version one – action state reinforcement learning
Our first version of the arm training program will introduce the basic framework, and use the most primitive form of machine learning, which is to just try random movements until the program finds something that works.

## Slide 23: Teaching the robot arm

## Slide 24: Teaching the robot arm
Adaptive learning rate
We insert a line at each update just after where we calculate the reward, as shown here:
state, reward = robotArm.step(action,learningRate) # insert this new line to try an adaptive learning rate
learningRate = (100-reward)/2.5

## Slide 25: Teaching the robot arm
The maximum reward for reaching the goal is 100 points. We want the learning rate to be an inverse ratio to the reward. As the reward gets bigger, the learningRate gets smaller. I also added the learning rate to the data recording, and created the following diagram from the results. You can see that the training action converged much faster. After a number of trials, it averages about four times as fast as the random approach we used in the first example. You can see the learning rate approaching zero as the reward nears 100:

## Slide 26: Teaching the robot arm

## Slide 27: Teaching the robot arm
Q-learning implementation
In Q learning, we develop a overall value of a set of actions that together result in the robot reaching its goal. This total value of a valid path to the goal is called Q.
We add a discount factor that penalizes longer paths; a shorter path is better. This discount factor is usually called by the Greek letter Gamma. The discount is a number less than 1 (usually 0.9 or so), and it is one of our tunable parameters. Imagine that we are at the goal:

## Slide 28: Teaching the robot arm
we get the full reward, 100 points, and the discount is 0. Then we move back to the state before we get to the goal, that is one step away. We multiply it by 0.9, so it gets 9/10 of the reward (90 points). The next space, two steps back, gets the reward from the 1-step space (90 points) times the discount factor (Gamma), which is 0.9 x 90 or 81. So each step back from the goal gets a bit less of the reward. A path with 10 steps gets more points than a path with 20 steps.

## Slide 29: Genetic algorithms
The main problem with Q-learning is that we have a very large number of possible states, or positions, that the robot arm can be in. This means that gaining a lot of knowledge about any one position by repeated trials is very difficult.
We are going to introduce a different approach using genetic algorithms to generate our movement actions.

## Slide 30: Genetic algorithms
Moving the robot arm requires coordination of three motors simultaneously to create a smooth movement.
What if we had a way of trying different combinations of motor movement, and then competing them against one another to pick the best one. It would be some sort of Darwinian survival of the fittest for arm movement scripts.
We are managing our gene pool to create a solution to a problem by successive approximation
We want to keep a good mix of possibilities that can be combined in different ways to solve moving our arm to its goal:

## Slide 31: Genetic algorithms

## Slide 32: Other robot arm machine-learning approaches
Google’s SAC-X
SACX program, which stands for Scheduled Auxiliary Control, they surmise that it can be quite difficult to assign reward points to individual movements of the robot arm.
They break down a complex task into smaller auxiliary tasks, and give reward points for those supporting tasks to let the robot build up to a complicated challenge. If we were stacking blocks with a robot arm, we might separate picking up the block as one task, moving with the block in hand as another, and so on.

## Slide 33: Other robot arm machine-learning approaches
Google referred to this as a "sparse reward“ problem if they only did reinforcement on the main task, stacking a block on on top of another. You can imagine in the process of teaching a robot to stack blocks that there would be thousands of failed attempts before a successful move resulted in a reward.

## Slide 34: Other robot arm machine-learning approaches
Amazon Robotics Challenge
Amazon has sponsored the Amazon Robotics Challenge, where they invited teams from universities in to use robot arms to pick up items off a shelf and, you guessed it, put them into a box. When you consider that Amazon sells almost everything imaginable, this is a real challenge.
In 2017, a team from Queensland, Australia won the challenge with a low-cost arm and a really good hand tracking system.

## Slide 35: Outline
Natural language processing
Reasoning from context
Understanding intent
Speech recognition (speech to text)
Text to speech
Call and response dialog for knock-knock jokes

## Slide 36: Technical Requirements
Mycroft Open Source Voice Assistant (http:/ / mycroft. ai)
Python 3.2
I used the Google DIY Voice Kit

## Slide 37: Robot speech recognition
We need the robot to be able to hear, or have the ability to convert sound into a digital form. We need to process sounds into words, which is to say, turn sounds into text.
We do not want to use canned or memorized speech commands, but rather have the robot be able to do some natural language processing (NLP) to create a form of robot understanding of the spoken word.

## Slide 38: Robot speech recognition
Our steps for the chapter are as follows:
1. Receive audio (sound) inputs.
2. Convert those sounds into text that the robot can process.
3. Use processing on those text words to understand the intent of the speaker.
4. Use that intent as a command to perform some task.

## Slide 39: Robot speech recognition
5. Provide verbal responses in the form of spoken words (text to speech) back to the operator to confirm the robot heard and understood the command.
6. Create a custom verbal interface that both tells and responds to knock-knock
jokes.

## Slide 40: Robot speech recognition
Speech to text
We will be using Mycroft, an open source voice activated digital assistant that is adept at understanding speech and is easily extended for new functions and custom interfaces.

## Slide 41: Robot speech recognition
The process we will use for voice interaction with the robot follows this script:
1. Wake word (Hey, Albert)
2. Pause for the robot to make a beep sound to show it is listening
3. Command or query from human (move forward one step)
4. Robot responds verbally (moving forward six inches)

## Slide 42: Robot speech recognition
How does the robot recognize the wake word? The speech system we will be using, the open source system Mycroft, uses one of two methods. The first is a phoneme recognition system called Sphynx. What the heck is a phoneme? You can understand that words are made up out of individual sounds, which we roughly assign to letters of the alphabet.

## Slide 43: Robot speech recognition
What is the other method for receiving the wake word? Mycroft can also use a trained neural network that has been taught to recognize entire words all at once by their spectral power graph.
What is a spectral graph? Your voice sound is not one frequency of sound energy – it is a complex congregation of different frequencies produced by our mouths and vocal cords.

## Slide 44: Robot speech recognition
If we spoke in pure frequencies, we would sound like a flute- pure tones at mostly one frequency. We can use a process called a fast fourier transform to convert a selection of speech into a graph that shows the amount of energy (volume) at each frequency. This is called a spectral plot or spectral graph. The low frequencies are at the left, and higher frequencies at the right.

## Slide 45: Robot speech recognition
Most of human speech energy is concentrated between frequencies between 300 Hz and 4,000 Hz.
Each word has a unique distribution of sound energy amounts in these frequencies, and can be recognized by a neural network in this manner:

## Slide 46: Robot speech recognition

## Slide 47: Robot speech recognition
Both the phoneme method and the neural network method use spectral plots to recognize sounds as words, but the phoneme process divides words into individual sounds, and the neural network listens and recognizes the entire word all at once.

## Slide 48: Robot speech recognition
Why does this make a big difference?
The phoneme system can be developed to recognize any word in English without reprogramming or retraining
The neural network has to be trained on each word individually, and hopefully by a lot of different speakers with a lot of different accents.

## Slide 49: Robot speech recognition
The Mycroft system then transfers that audio data over the internet to the Google
online speech-to-text engine
This is a quick way to resolve the problem of our little Raspberry Pi not having enough processing power or storage to have a robust speech recognition capability.

## Slide 50: Robot speech recognition
What goes on the in the Google Cloud?
The STT engine breaks the speech down into phonemes (sounds) and uses a neural network to assign the most probable graphemes (letters) to those sounds. The output would be spelled out more phonetically than want to receive.

## Slide 51: Robot speech recognition
Intent
The natural language processing we are doing has one aim, or goal. We are giving commands to our robot using a voice interface.
The TinMan robot to listen and understand commands using a open source artificial intelligence package called Mycroft.

## Slide 52: Robot speech recognition
Mycroft is a version of a digital assistant similar to Siri from Apple or Alexa from Amazon, in that it can listen to voice commands in a mostly normal fashion and interface those commands to a computer. We are using it because it has an interface that runs on a Raspberry Pi 3. Here we go.

## Slide 53: Robot speech recognition
Mycroft
Hardware

## Slide 54: Robot speech recognition
Mycroft software
While there are several ways to install Mycroft, we have to put Mycroft on top of the other
software we have already. Since Mycroft has to get along with the ROS, and all of the
artificial intelligence packages we installed, such as TensorFlow, Theano, and Keras, it is
better that we use the git clone method to download the source code and build Mycroft
on the Raspberry Pi:

## Slide 55: Robot speech recognition
git clone https://github.com/MycroftAI/mycroft-core.git
cd Mycroft-core
bash dev_setup.sh
Mycroft will create a virtual environment it needs to run. It also isolates the Mycroft
package from the rest of the packages on the Raspberry PI.