## Slide 1: Dr.SNS RAJALAKSHMI COLLEGE OF ARTS AND SCIENCE (AUTONOMOUS) COIMBATORE-641049 Accredited by NAAC(Cycle III) with “A+” Grade Recognised by UGC, Approved by AICTE, New Delhi and Affiliated to Bharathiar University, Coimbatore.
DEPARTMENT OF COMPUTER SCIENCE
21PCS101:Artificial Intelligence for Robotics
I YEAR - I SEM
TOPIC – SLAM
UNIT 5 – SLAM

## Slide 2: Outline
Mobile robot navigation concepts
Vision processing
The Floorfinder algorithm
Vision-based navigation using neural networks
Object recognition and navigation with neural networks
Decision tree-based logic
Goal-oriented behaviors
Robot command and control

## Slide 3: Technical Requirements
We require the Robot Operating System (ROS) for the chapter. The uses the Kinetic Kame release: http:/ / wiki. ros. org/ kinetic/ Installation

## Slide 4: Task analysis
We will set this as a challenge, then, to accomplish our task without making a map. What
else do we need to do?
Navigate the room avoiding obstacles (toys and furniture) and hazards (stairs)
Find a toy
Pick up the toy with the robot arm
Carry the toy to the toy box
Put the toy in the toy box
Go and find another toy
If there are no more toys, then stop

## Slide 5: Task analysis
The appropriate next step, whether we are designing robots or invading castles, is to do some brainstorming. How would you go about solving this problem?
We could use SLAM and make a map, then locate the robot on the map, and use that to navigate. But to really do SLAM, we need more sensors.

## Slide 6: What is SLAM?
SLAM is a common methodology for navigating indoor robots.
The first problem we have in indoor robot driving is that we don't have a map.
The second problem we have is that we have no frame of reference to locate ourselves – GPS does not work indoors.
That is two problems – we need a map, and then we need a way to locate ourselves on that map. While SLAM starts with the letter “S” for Simultaneous, in truth, most robots make a map, store it away, and then drive on it later

## Slide 7: What is SLAM?
How does SLAM work?
The sensor usually associated with SLAM is the spinning LIDAR. You can think of LIDAR as a laser radar – it uses a laser to measure the distance to objects, and spins in a circle to collect data all around the robot.
You can actually get a very small robot LIDAR, called the Rplidar, for around $100.00, and use it to make maps. There is an excellent ROS package called Hector Mapping that makes using this LIDAR fairly straightforward.

## Slide 8: What is SLAM?
You will find that SLAM is not a reliable process, and will require several fits and starts to come up with a map that is usable.
Once the map is created, you have to keep it updated if anything in the room changes (such as, for instance, grandchildren leaving toys everywhere).

## Slide 9: What is SLAM?
An illustration of a SLAM Map. The robot uses 500 particles for each LIDAR sample to estimate which changes in robot position best line up the lidar data with the data in the rest of the map. This is one of my earlier robot projects.

## Slide 10: What is SLAM?
Summarize SLAM as follows:
The robot takes a measurement of the room by sweeping a laser rangefinder in a circle. The data returned is a list of distance measurements, where the angular measure is a function of the position in the list.
If we have a list of 360 measurements in a circle, then the first number in our list is 0 degrees, the next is 1 degree, and so on.
We can extract features in the LIDAR data by looking for corners, edges, jumps, and discontinuities.

## Slide 11: What is SLAM?
Summarize SLAM as follows:
We look at the angle and distance to each feature from succeeding measurements, and create a function that gives the best estimate of how much the robot moved. We use that information to transform the LIDAR data from the sensor-centric coordinate system to some sort of room coordinate system, usually by assuming that the starting position of the robot is coordinate 0,0.
Our transform, or mathematical transformation, will be a combination of translation (movement) and rotation of the robot's body frame.

## Slide 12: What is SLAM?
Summarize SLAM as follows:
One way of estimating this transform is to use particles. We create samples of the robot's movement space of every point possible that the robot could have moved, and randomly place dots along all points. We compute the transform for each of these samples, and then test to see which sample best fits the data collected. This process is called a particle filter

## Slide 13: What is SLAM?
The weaknesses of SLAM for our purposes include the following:
The need for some sort of sweeping sensor such as LIDAR, which are expensive,
mechanically complicated, and generate a lot of data. We want to keep our robot
cheap, reliable, and simple.

## Slide 14: What is SLAM?
SLAM works better if the robot has wheel odometers, which don't work on
tracked vehicles such as our TinMan. Tracked robots can also be referred to as
Skid steered vehicles, because the tracks slide or skid over the surface in order to
turn – we don't have Ackerman steering, like a car with wheels that point. When
the track skids, it is moving over the surface without turning, which invalidates
any sort of wheel odometry, which assumes that the wheels are always turning
in contact with a surface.

## Slide 15: What is SLAM?
SLAM does not deal with floorplans that are changing. The TinMan robot has to
deal with toys being distributed around the room, which would interfere with
LIDAR and change the floorplan that SLAM uses to estimate position. The robot
is also changing the floorplan as it picks up toys and puts them away.
SLAM is somewhat computationally expensive.
SLAM has problems if data is ambiguous, or if there are not enough features for
the robot to estimate changes on. I've had problems with featureless hallways as
well as rooms that where highly symmetrical.

## Slide 16: What is SLAM?
Alternatives for navigation
We could do a process called structure from motion to get depth information out of our single camera, and use that to make a map.
Structure from motion requires a lot of textures and edges, which houses may not have. It also leaves lots of voids (holes) that have to be filled in the map.
Structure from motion uses parallax in the video images to estimate the distance to the object in the camera's field of view. The video image has to have a lot of detail in it so that the process can match points from one video image to the next.

## Slide 17: What is SLAM?
Alternatives for navigation

## Slide 18: What is SLAM?
The following diagram shows the ability of various selection attributes (color, hue, saturation, and luminosity) as a tool to perform floor finding for our robot. The Hue attribute seems to provide the best results in this test. I tested it on another image to be sure it was working. It seems to be missing the baseboards.
We select all of the pixels that match our floor colors and paint them green – or, to be more correct, we create a mask region in a copy of the image that has all of the pixels we want designated somehow.

## Slide 19: What is SLAM?
Performing an erode function on the masked data can help in this regard. There may be small holes or noise where one or two pixels did not match our carpet colors exactly – say there is a spot where someone dropped a cookie. The Erode function reduces the level of detail in the mask by selecting a small region

## Slide 20: What is SLAM?
My version of the floor finder algorithm has the steps illustrated here. Note that it does a very good job in this case of identifying where it is safe to drive. The projected paths are
required to prevent the robot from trying to drive up the wall. You get bonus points if you can identify the robot in the corner.

## Slide 21: What is SLAM?

## Slide 22: What is SLAM?
The image shows the technique for measuring distance in the robot camera field of view. The object is located four feet away from the robot base along the tape measure. Note that the robot easily sees its own treads in the foreground. TinMan uses a 180-degree fisheye lens on an HD-capable web camera

## Slide 23: Neural networks

## Slide 24: Processing the image

## Slide 25: Processing the image
Our neural network is a nine-layer convolutional neural network very similar to the toy/not toy detector we made before.
However, in our final step, rather than being a binary output determined by a binary classifier, we will use a Softmax classifier with three outputs – forward, left, or right turns.
We can actually make more categories if we want to, and have easy right and hard right turns rather than just one level of turns. We could even add a "back up" category, but let's try with the simple model first, and have three outputs.
Remember that the number of output categories must match our training set labels exactly.

## Slide 26: Processing the image
Our CNN has nine layers. The first six are pairs of convolution networks with max pooling layers in between. This lets the network deal with incrementally larger detail in the image.
The final two layers are fully connected with ReLU (Rectifier Linear Units) activations.
Remember, that ReLU only takes the positive values from the other layers.
Our final layer is a Softmax classifier with three outputs:

## Slide 27: Processing the image

## Slide 28: Training the neural network for navigation
we build our actual neural network by instantiating the ConvNet object that actually builds our CNN in Keras. We set up the optimizer, which is ADAM, a type of adaptive gradient descent. ADAM stands for Adaptive Moment Estimation. ADAM acts against the error gradient like a heavy ball with friction – it has some momentum, but does not pick up speed quickly

## Slide 29: Outline
An expert system
Random forests

## Slide 30: Technical Requirements
We will be using PyKE – the Python Knowledge Engine – as our expert system

## Slide 31: Decision trees
The concept of a decision tree is fairly simple. You are walking down the sidewalk, and come to a corner. Here you can go right, turn left, or go straight ahead. That is your decision. After making the decision – turn left – you now have different decisions ahead of you than if you turned right. Each decision creates paths that lead to other decisions:

## Slide 32: Decision trees

## Slide 33: Decision trees
We can call each of these possible decisions a branch, the state we are in after making the decision is a leaf, and the entire conceptual structure is a decision tree.
There are two ways to deal with a decision tree
  Forward Chaining
  Backward Chaining

## Slide 34: Decision trees
The third technique? No one says we can’t do both – we could combine both forward and backward chaining and meet somewhere in the middle.
The choice of decision tree shapes, chaining techniques, and construction are based on:
What data is available?
What information is known or unknown?
How is the path scored or graded?

## Slide 35: Decision trees
There are also different kinds of solutions for path planning and decision trees. If you were given unlimited resources, the biggest computer, perfect knowledge in advance, and are willing to wait, then you can generate an optimal path or solution.

## Slide 36: What do we mean by pruning?
One great use for a decision tree process is FDIR – Fault Detection, Isolation, and Recovery. This is a typical function of a robot. Let’s make a decision tree for FDIR in the case of our Tinman robot not moving.
A special form of decision tree called a Fishbone diagram, or Ishikawa diagram. This diagram is named after its inventor, Professor Kaoru Ishikawa from the University of Tokyo. In his 1968 paper, Guide to Quality Control, the Fishbone diagram is named because of its shape, which has a central spine and ribs jutting off on either side. I know, the metaphors are getting deep when we have a decision “tree” in the shape of a “fish”.

## Slide 37: What do we mean by pruning?
Here is my Fishbone diagram for the problem of the robot not moving:
we solved our problem almost entirely by pruning branches and leaves off our tree until only one path was left, or we arrived at our goal.

## Slide 38: What do we mean by pruning?

## Slide 39: Self-classifying decision trees and AI tools

## Slide 40: Entropy
There is another type of process for creating decision trees and subdividing data into categories. That is called the Entropy model, or information gain.
Entropy is a measurement of the amount of disorder in the sample of data provided. We can also call this process information gain, since we are measuring how much each criteria contributed to our knowledge of which class it belongs to.

## Slide 41: Entropy
The formula for entropy is a negative log base 2 function, that is still primarily looking at the probability of a class belonging to a population, which is just the number of individuals belonging to each class divided by the total number in the sample:
Entropy = Σ_(i=1)^c▒[-p_i*log2(p_i)]
To substitute entropy as our group criteria in our program, we only have to change one line:
dTree = tree.DecisionTreeClassifier(criterion ="entropy")

## Slide 42: Entropy

## Slide 43: One hot encoding
A rather troubling relationship, which is an artifact of how we encoded our data as a sequential set of numbers. This is implying relationships and grouping that don’t really exist. How can we correct for this?
As a matter of fact, there is a process for handling just this sort of problem. This technique is widely used in AI programs, and is a “must have” tool for working with classification, either here in the decision tree section, or with neural networks. This tool has the strange name of “one hot encoding”.

## Slide 44: One hot encoding

## Slide 45: Random forests
I really wanted to add this section on random forest classifiers, just because the name sounds so darn cool. There has even been talk of extreme random forests. While I may have been accused of stretching metaphors to the breaking point, this time the name may have inspired the software.
If you wanted to take advantage of the simplicity and utility of decision trees, but wanted to handle more data, more uncertainty, and more classes, you can use a random forest, which, just as the name indicates, is just a whole batch of randomly generated decision trees.

## Slide 46: Grid searching and A* (A-Star)
A problem related to classification, and that is grid searching and path finding. We will be learning about the famous and widely used A* (pronounced A-Star) algorithm. This will start with grid navigation methods, topological path finding, such as GPS route finding, and finally, expert systems. You will see that these are all versions and variations on the topic of decision trees that we have already learned.

## Slide 47: Grid searching and A* (A-Star)

## Slide 48: Grid searching and A* (A-Star)

## Slide 49: Grid searching and A* (A-Star)
One approach is to use a wavefront method

## Slide 50: Grid searching and A* (A-Star)
Greedy Best First approach

## Slide 51: Grid searching and A* (A-Star)
shortest path

## Slide 52: The A* algorithm
A* has its origins with Shakey the Robot at Stanford University back in 1968.
This was one of the first map navigating robots. Nils Nilsson and his team were trying to find a method to navigate Shakey around the hallways at Stanford, and started trying different algorithms.
The first was called “A1”, and so forth. After several iterations, the team decided that a combination of techniques worked best. In computer science, A* means the letter A followed by anything else, and thus the A-Star was named.

## Slide 53: The A* algorithm
The concept of the A-Star process is very much like what we have already been doing with
our other path planners. Like the wavefront planner, we start by considering the neighbors
around our starting location
We will compute a heuristic, or estimate, for each square
based on two factors: the distance from the starting location and the distance in a straight
line to the goal. We are going to use these factors to find the path with the lowest
cumulative cost.

## Slide 54: The A* algorithm
We calculate that cost by adding up the heuristic value for each grid
square that is part of the path. The formula is:
F(n) = g(n) + h(n)
where: F = contribution of this square to the path cost, g(n) = distance from this square to
the start position along the path chosen (that is, the sum of the path cost), and h(n) is the
straight line distance from this square to the goal.
This value represents the cost or contribution of this square if it were a part of the final
path. We will select the square to be part of the path which has the lowest combined cost.
As with the wavefront planner ,we keep track of the predecessor square, or the square that
was traversed before this one to reconstruct our path:

## Slide 55: The A* algorithm

## Slide 56: The A* algorithm
The preceding diagram illustrates the A* (A Star) algorithm. Each square is evaluated
based on the sum of the distance along a path back to the start(G), and an estimate of the
remaining distance to the goal (H). The yellow squares represent the path selected so far.

## Slide 57: D* (D-Star or Dynamic A*)
The A* process is only run one time to plan a route for a robot, before it begins to move. D*, a dynamic replanning process, is constantly updating the robot’s path as new information becomes available.
The D* algorithm allows for replanning by adding some additional information to each grid square. You will remember that in A*, we had the G-Value (distance to the start along the path), and the H-Value (straight line distance to the goal).
D Star adds a tag to the square that can have several possible values. The square’s tag could be NEW, for a new square that had never been explored before. It could be OPEN, for tags that have been evaluated and are being considered as part of the path. CLOSED is for squares that have been dropped from consideration.

## Slide 58: D* (D-Star or Dynamic A*)
The next two tags are RAISED and LOWERED. The RAISED flag is set if a
sensor reading or additional information caused the cost of that square to increase, and
LOWERED is the opposite. For LOWERED squares, we need to propagate the new path cost to the neighbors of the now lower cost square, so that they can be re-evaluated. This may cause tags to change on the neighboring squares. Raised squares have increased cost, and so may be dropped from the path, and Lowered squares have reduced cost, and may be added into the path.

## Slide 59: D* (D-Star or Dynamic A*)
Another major difference between D* and A* is that D* starts at the goal and works backward toward the start. This allows D* to know the exact cost to the target – it is using the actual path distance to the goal from the current position and not a heuristic or estimate of the distance to go, like A* did.

## Slide 60: GPS path finding does not use a map
An amazing amount of work has gone into making our current crop of GPS systems small, lightweight, and reliable. Of course, they are dependent on up-to-date information in the database:

## Slide 61: GPS path finding does not use a map

## Slide 62: Outline
Transaction-based conversation
Designing a chatbot
Natural language processing (advanced)
Simulation tools
Monte Carlo modeling

## Slide 63: The Turing test
Alan Turing proposed his famous test, which he called The Imitation Game in a paper titled Computing Machinery and Intelligence, published in 1950 in the journal Mind – A Quarterly Review of Psychology and Philosophy
Retrieva-based chatbots rely on stored phrases and words, and use the software decision making to select which reply is most appropriate. There may be some keyword recognition and noun-subject insertion involved, but the main action is to select the most appropriate phrase.

## Slide 64: The Turing test
Generative-based chatbots are making up new sentences based on parts of speech and the robot’s divination of your intent. They can be thought of as machine translation engines that translate the input (your text or speech) into an output (the robot’s reply). As you might imagine, the generative type chatbot is far more difficult to achieve, which is why we will be using a retrieval-based approach.

## Slide 65: The art and science of simulation
What is simulation?
A simulator is a computer model of the physical world.
familiar with flight simulators, which provide the sensations and interactions of flight without leaving the ground.
Another type of simulation is called a Monte Carlo model. The Monte Carlo method uses probability theory to replace sophisticated physical models with a variation of random numbers that approximates the same result.

## Slide 66: The art and science of simulation

## Slide 67: The art and science of simulation

## Slide 68: An emotion state machine
What is a state machine?
We covered state machines in the section on systems engineering
– state machines are a technique for understanding or modeling automation or computer
programs.
A state is a set of conditions that exist at the present. I like to think of a state as
being a set of functions that are constrained by limits.
The machine (our robot) changes from state to state based on some event that causes the state to change.

## Slide 69: An emotion state machine
Now let’s think about our model of robot emotions. We can start by listing what emotions
we want our robot to have:
  Happy
  Welcoming
  Friendly
  Curious
  Fresh
And the opposites of those emotions:
  Sad
  Distant
  Stranger
  Frustrated
  Tired

## Slide 70: An emotion state machine

## Slide 71: An emotion state machine
What is a state machine?
We covered state machines in the section on systems engineering
– state machines are a technique for understanding or modeling automation or computer
programs.
A state is a set of conditions that exist at the present. I like to think of a state as
being a set of functions that are constrained by limits.
The machine (our robot) changes from state to state based on some event that causes the state to change.